## Slide 1: TEOA Lean Essentials Advanced Boot Camp
Lean Principles
Notes: 1
9:10 start 9:35 end
30 minutes

## Slide 2: The Five Lean Principles
  Specify what creates value from the customer’s perspective
  Identify all steps across the whole value stream
  Make those activities that create value flow
  Make only what is pulled by the customer just in time
  Strive for perfection by continually removing successive layers of waste
  Womack & Jones, Lean Thinking
This set of principles is the “True North”
What is a “True North”?
Notes: Specify what creates value from a customers perspective... This is usually approached with the question „What will the customer pay for?“ Lean must begin with a determination of what value the company provides. One of the most popular conceptions in Lean is that all employees must learn to see with the eyes of the customer
Identify all steps across the whole value stream... A value stream is all all of the activities, both value-added and non-value-added, to go from mew material to to finished product. We could add from order to cash and from product concept to product launch to this to be more inclusive. A process called value mapping is used to accomplish this step. For more on this, see the Learning to See class/book from the Lean Enterprise Institute.
Make those actions that create value flow... One-piece flow is the ultimate objective, with first-in-first-out (FIFO) flow next, then finally pull: no push of product or activity. The implication here is that the non-value-added activities will be eliminated, which is one of the focuses of Lean: the elimination of waste. Part of the focus of this class is to explore what this step, and the next one, really means, define the various factors that effect how well this approach will work in various environments of production, and suggest suggest approaches and solutions based on the environment.
Only make what is pulled by the customer just in time... This drives us to more of a make-to-order environment, which from a supply chain perspective is different than the solution present in the Toyota Production System. See bold comment above.
Strive for perfection by continuously removing successive layers of waste... This is the continuous improvement that is often talked about when discussing Lean. Note that implementing continuous improvement techniques without the first four principles will probably bring disappointing results. It can not be over-emphasized that Lean is a complete system of operation, not a quest for “low-hanging fruit“.
True North… is the internal compass that guides you successfully through life. It represents who you are as a human being at your deepest level. It is your orienting point – your fixed point in a spinning world – that helps you stay on track as a leader in a spinning world. (Bill George, www.truenorthleaders.com).
True North… is often cited within the topic of Lean within the context of management considerations for success.

## Slide 3: Comment - The Five Lean Principles
“Note that implementing continuous improvement techniques without the first four principles will probably bring disappointing results.
It can not be over-emphasized that Lean is a complete system of operation, not a quest for “low-hanging fruit”.
  Kerber & Dreckshage (along with many others), Lean Supply Chain Management Essentials
Notes: Spot kaizen can cover low-hanging fruit, and each value stream / team will be able to see short term impacts and benefits potentially, but need true transformation in order to sustain long term gains in all performance metrics.

## Slide 4: Two Kinds of Kaizen
FLOW KAIZEN
PROCESS KAIZEN
Senior Mgmt.
Front Lines
Focus
  Womack & Jones, Learning to See
Management Doing Kaizen
(Value Stream Improvement)
(Elimination of Waste)
Notes: Process kaizen – elimination of waste – ask for examples from the class of process kaizen events that they have implemented – could be a 5S activity, or even a cell layout improvement to reduce transportation
Flow kaizen – value stream improvement – Management doing kaizen – need them involved in order to ensure 5 lean principles being followed, emphasis on management involvement  critical to the success of transformation as they support the flow kaizens and remove barriers – these activities are focused on one piece flow and producing only what the customer needs at their pull
Flow on the left, process on the right on the X axis

## Slide 5: What is a Lean Value Stream?
  Makes only what the next process needs when it needs it
  Links all processes – from final customer back to raw material:
      in a smooth flow,
      without detours,
      and generates the shortest lead time, highest quality & lowest cost
  Womack & Jones, Learning to See
ESSENTIAL 1
Notes: Poll the class for definitions of Lean Value Stream before showing the results
Can ask the class what is flow? – think of a stream where water is flowing at a steady pace
What are detours> -- detours are waste! Good opportunitiy to review the 8 types of waste covered in Lean Foundations; ask the class what is the worst waste? Continue taking answers until Overproduction, and explain how it leads to all of the other wastes – same stream example could be a beaver creating a dam to stop the flow or rocks in the stream
Ultimately a lean value stream should produce exceptional financial returns

## Slide 6: Value Stream Design…
… is the process of developing a detailed vision (map) and plan to create a Lean Value Stream in accordance with the Five Lean Principles.
Note: Value Stream Mapping is Lean Principle #2
Notes: Value stream design is focused on flow kaizen – one can identify a lot of process improvements of process kaizens on a current state map without looking to create flow – VS design is all about flow and pull
There is a structured approach that we will follow to help guide us and help us design the best future state map we can as of now

## Slide 7: What Is Value Stream Mapping?
Establish a culture of continuous improvement, everyday by everyone
Six
Sigma
Cell
Design
Voice of Customer (VOC)
Safety
Production Preparation Process (3P)
Fast
Response
5S and
Visuals
Quick Change
Over (QCO)
Mistake Proofing
Standard
Work
Material Replenishment and Flow
Process Improvement Management (PIM)
Quality Control Process Charts
(QCPC)
Total Productive Maintenance (TPM)
Total Employee Involvement
We are Committed to Delivering an Extraordinary Customer Experience
Value
Stream
Mapping
Create Flow
Establish Pull
High Level Plan
Map the Value Stream
Pursue Perfection
Definition: A visual map that creates an end-to-end picture of a plant’s current or future material and information flow at the product family level
What is a Product Family?
Notes: value stream is made up of parts from a product family, defined as a set of parts that go through roughly the same processes.
Product families are different than process families (associated with resources that are shared with multiple value streams). We cover that in more detail later in this class.
Spark conversation on VSM – why is it the steps to get into the house????
  Should be the starting point for all of the other transformation activities – can complete activities around the orange foundations without creating flow, but the blue tools should all be elements that will help you transform – do not know which tools to use until you create a value stream design, which is why these are the steps to get into the house!

## Slide 8: Important Definitions
Process: Defined between two points where inventory stops and accumulates
Cycle Time (C/T): How often a part actually is completed by a process (sometimes referred to as Drop-Off Rate). Also, the time it takes an operator to go through all of their work elements before repeating them.
Value Creation Time (VCT): Time of those work elements that actually transform the product in a way that the customer is willing to pay for. Some times referred to Value Adding Time (VAT)
Lead Time (L/T): The time it takes one piece to move all the way through a process or a value stream, from start to finish.
40 seconds
2 hours
40 seconds
L/T through the process
VCT (VAT)
VCT (VAT) = L/T through the process
Notes: A very important page. Take the necessary time
Blank the page and ask the audience for the definition of every one of these terms above:
  Process: it is very important to define a process being activities defined between points where inventory stops and accumulates. Highlight the difference between one machine being a process and three machines being a process because there is no inventory that stops and accumulates between the three machines
  Drop off rate: also known as Cycle Time, how often you catch a part out of the process. Discuss the difference between drop off rate at the machine level and at the process level
  Value Creation Time: time of those work elements that actually transform the product in a way tat the customer is willing to pay for.
  Lead time: that’s what we’re shooting for.. Reduction of lead time from raw material to finished goods. In a manufacturing system one of the most important things is the comparison of the overall lead time. for example the time it takes from order to delivery, the lead-time through the manufacturing plant. Reducing the lead time will save cost of capital (reduction in storage equipment, reduction in WIP) and also cost of good (reduction in labor to look after excess inventory etc….
  Should have multiple definitions of Lead Time, Customer Impact lead time, Production LT, etc.

## Slide 9: Creating A Future State VSM
Select a product family
Map the current state
Design the future state
Deployment
Plan and Implementation
Focus on the production of a single product from beginning to end
Develop an understanding of what happens today
  Information
  Material
  Interactions
Design a “LEAN VALUE STREAM”
  Create flow; pull where you can not
  Follow the “ESSENTIALS”
Create a deployment plan (project, timing, resources) to achieve the future state design
Notes: This is the process for all value stream mapping
It is not enough to have pretty pictures on the wall; a future state map without a plan is pure waste

## Slide 10: True North – Value Stream Mapping
  What is the TAKT time?
  Will you build to a finished goods supermarket, or directly to shipping?
  Where can you use continuous flow processing?
  Where will you need to use supermarket pull systems to control production of upstream processes?
  At what single point in the production chain (the “pacemaker process”) will you schedule production?
  How will you level the production mix at the pacemaker process?
  What increment of work will you consistently release and take away from the pacemaker?
  What process improvements will be necessary for the value stream to flow as your future-state design specifies?
      Womack & Jones, Learning to See
Always in this order
Back-tracking at any point allowed & encouraged
ESSENTIAL 2
Notes: These are the steps to design a lean future state
Directly out of Learning to See
Should always be asked in order, but sometimes, after answering certain questions or as you progress through the design, you will need to back track and ask the questions again – we will explore this later in the week but as a preview – if you add more part numbers into the design, your takt will change, so you will need to go back and answer question 1
These quetions are going to be the flow for the week and we will answer each one for the Volcano case study, and for your real example

## Slide 11: But Value Streams can be Complicated
What about:
Highly variable demand?
Product portfolio complexity?
  Mix
Low volume?
Shared resources within and across value streams?
Others???
Acme example from Learning to See is very simple
CHAOS
Notes: The real world is more complicated than the example outlined in learning to see, how do you handle all of these different situations? All of these bullets can lead and contribute to CHAOS! Chaos is not good! We want to try and mitigate chaos, and ELIMINATE chaos where we can
Upstream parallel processes, takt time in hours / days vs seconds,

## Slide 12: The Chaos Graph
  Duggan, Creating Mixed Model Value Streams
As Lead Time Increases, the Amount of Chaos Increases – Seemingly Infinitely
Chaos
1 Month
1 Day
2 Month
3 Month
Lead Time
Notes: The opportunity for chaos is nearly non-existent with short lead times
You can explain a simple situation of how many things can go wrong in the next 1 minute? What about in the next week? The next month? The next year? There are so many more failure modes or opportunities for things to go wrong the longer the lead time
Ask the audience how they define chaos – customer demand spikes, expedites, plan changes, more changeovers, etc.
More time more money, etc. for things to go wrong

## Slide 13: The Value Streams Chaos Function
Flexibility is Good – to a Point
Some Flexibilities are Better than Others
Infinite Flexibility Creates Infinite Complexity
SIMPLIFY…
“LESS SHARED IS BETTER SHARED”
ESSENTIAL 3
Notes: Good flexibility: Is approaching 0 changeover time a good thing? --YES
Not so good flexibility: 50 machines that I can run this part on? Good thing? – Maybe not – but this is a planner’s dream!!
Simplify wherever we can – this may mean dedicating machines, shifts, or resources to run specific part numbers / families

## Slide 14: Mapping Information and Material Flow
Supplier
Production Control
Customer
Maps material flow from left to right (down stream)
Maps information flow from right to left (up stream)
Material Flow
Information Flow
Notes: There are two flows represented on the map
  The Material flow that goes from left to right
  The information flow that goes from right to left
Most of the conventional maps focus on material flow only. The advantage of this map is that it superimposes the information flow over the material flow, a key difference of significant importance because information flow is often responsible for the performance of the system
A VSM map without information flow is an incomplete map and misses the point.
Explain upstream vs downstream – downstream is closer to the customer, upstream is closer to the supplier – no need to discuss pacemakers at this point, keep it very simple

## Slide 15: Developing A Current State VSM – Tips
Do it yourself
Use a pencil
Do a quick review
Do detailed analysis
Gather your own data; don’t believe data provided by others
If you see for yourself, you gain a true understanding
Do not divide the flow, as you need to understand the end-to-end activity
Sketch the flow as you walk the process
Modify as appropriate
Focus on the flow and interrelationships, not on making it look pretty
Walk quickly and get a sense of the flow and sequence of processes
Walk the process from customer requirements back to inputs (for example, from shipping dock back to raw materials)
Capture all relevant process data as you go; for example:
  Cycle time
  WIP/wait time
  Changeover time
  Number of people
  Working time
Notes: Value stream mapping is an interactive tool.
Walk the audience through the steps of value stream mapping as laid out on the main slide
Why use a pencil and paper Vs electronic with Visio or iGrafx? – drawing it by hand and building up the map on paper aids discussion between team members. It is often during these discussions that important information about the process being mapped is discovered, debated, challenged etc.
Doing it via pencil / post it notes is a good idea because you will make a mistake!
You could spend weeks gathering every single piece of data in order to have a perfect CVSM – we do not need a perfect map! We just need enough detailed information to allow us to design an accurate lean future state – 80% is good enough!

## Slide 16: VSM Standard Icons (1/2)
Truck movement
Push arrow
Movement of goods to customer
Shop stock (controlled inventory)
Physical pull
Mfg process
Data box
Assembly
Outside source
Company name
C/O = _____
P/T = _____
Shifts = _____
Warehouse
Warehouse
Airplane
Train
Cross dock
Cross dock
Uncontrolled inventory
Material flow
First-In-First-Out sequence
FIFO
Notes: These are the VSM icons.
VSM is a language and it is important that one uses these icons in the mapping of the maps so that a team in China can exchange a design with a team in the US or England. Evey icon means something. Please pay great attention to the meaning and respect the convention
The most important symbols are: The process boxes, the external suppliers, or entities, the inventory traingle, the push arrow, and the supermarket / pull arrows.

## Slide 17: VSM Standard Icons (2/2)
Database(s)
Frequent small shipments
Signal kanban
Information source
Load leveling
Manual information flow
Electronic information flow
Schedule
Computer-generated report
OXOX
Production kanban
Withdrawal kanban
Telephone
Kanban arriving in batches
Kanban post
Other
Problem area
Change over
Worker
Go see Scheduling
Material flow
Notes: Likewise, please bring the audience attention to the information flow arrows, the kanban signals and the kaizen burst cloud
Make sure that these are in sync with LTS